AENG 510 Vehicle Electronics I

Fall Term, University of Michigan-Dearborn

# Course Overview: This course discusses the principles of electrical engineering and applications of electrical and electronic systems in automobiles. It is designed for non-EE majors.  Some automotive E/E applications are used for case study.

## General Information: Lecture: Wednesday 6:10-9:00 PM

Instructor: Professor Chris Mi, chrismi@umich.edu, Tel: 313-583-6434, Fax: 313-583-6336

Office: 226 ELB, Office hours: Tuesday 1:00-3:00pm, & Wednesday 4:00-6:00 PM

http://vlt.engin.umd.umich.edu/dashboard/ course number: AENG510, Enrollment key: 1234

You are REQUIRED to visit the web site every week and Check the website before you call or email for questions. Note HW/exam solutions and handouts will be posted at the course website.

Textbook: 	Principles and Applications of Electrical Engineering, A. Hambley, Third edition, 			Prentice Hall, 2002

Reference books:	1. Understanding Automotive Electronics, 5th Edition, W. B. Ribbens, SAE, 1998.			2. Auto Electricity and Electronics, Technology, J. Duffy, the Goodheart-Willcox 			   Company, 1998.

Grading:

40% - assignments

30% - midterm, Wed. October 26, 2004

30% - final exam, Wed. December 14, 2004

Grades are assigned approximately as follows: A (90-100), B (80-89), C (70-79), D (60-69), and E (0-59).

## Course Outline

| Week | Chapter(s) | Principles | Automotive case studies and examples |
| --- | --- | --- | --- |
| 1 | 1 | Introduction: current, voltages, power, energy, KCL, KVL, and basic circuit concepts | Overview of automotive electrical and electronic applications, automotive wiring and power supply, 14V vs. 42V systems |
| 2 | 2 & 3 | Resistor Circuits, Inductor, and Capacitor Circuits: series and parallel connections, voltage and current dividers, circuit analysis | Automotive lighting circuits, inductive loads (motors and solenoids), automotive EMC transients |
| 3 | 4 | Transient Circuit Analysis: RC and RL circuits. Matlab/Simulink simulation of circuit transients | Automotive inductive and capacitive discharge ignition circuits |
| 4 | 5 & 6 | Steady-State Sinusoidal Analysis and Frequency response: sinusoidal currents and voltages, complex impedance, AC analysis, filters, resonance and PSpice simulation of circuits | Telematics, radio/car phone, GPS, sensors, and digital filtering |
| 5 | 10 | Diodes: basic device physics, terminal characteristics, and analysis | Rectifier and Zener diodes in automotive E/E systems |
| 6 | 14 | Basic Amplifier Concepts and Operational Amplifiers | Analog circuits in automotive E/E systems |
| 7 | 12 & 13 | MOSFETs and Bipolar Junction Transistors (BJT) | Semiconductor devices and silicon integrated circuits in automobiles |
| 8 | 15 | Electromechanics: Magnetic circuits and transformers | Solenoids, actuators, and step motors |
| 9 | 16 & 17 | DC machines and AC machines | motors in EVs and HEVs |
| 10 |  | Analysis, simulation and design of ignition circuit |
| 11 |  | Alternators, starters, rectifier circuits, and dc-dc converters |
| 12 |  | EV, HEV and fuel cell vehicles, electric drive train design |